Computer Architecture
Basic Processor Design:
Physics, transistors, gates
Slides developed by Dr. Gary Tyson

---
Levels of abstraction
Quantum level, solid state physics
- Conductors, Insulators, Semiconductors.
- Doping silicon to make diodes and transistors.
- Building simple gates, boolean logic, and truth tables
Combinational logic: muxes, decoders
- Clocks
- Sequential logic: latches, memory
- State machines
- Processor Control: Machine instructions
Computer Architecture: Defining a set of instructions

---
Start with the materials: Conductors and Insulators
Conductor: a material that permits electrical current to flow easily. (low resistance to current flow)‏
  - Lattice of atoms with free electrons
Insulator: a material that is a poor conductor of electrical current (High resistance to current flow)‏
  - Lattice of atoms with strongly held electrons
Semi-conductor: a material that can act like a conductor or an insulator depending on conditions. (variable resistance to current flow)‏

---
Making a semiconductor using silicon
What is a pure silicon lattice?
A. Conductor
B. Insulator
C. Semi conductor
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e

---
N-type Doping
We can increase the conductivity by adding atoms of phosphorus or arsenic to the silicon lattice.
  - They have more electrons (1 more) which is free to wander…
  - This is called n-type doping since we add some free (negatively charged) electrons

---
Making a semiconductor using silicon
P
What is a n-doped silicon lattice?
A. Conductor
B. Insulator
C. Semi-conductor
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
This electron is easily
moved from here

---
P-type Doping
Interestingly, we can also improve the conductivity by adding atoms of gallium or boron to the silicon lattice.
  - They have fewer electrons (1 fewer) which creates a hole. Holes also conduct current by stealing electrons from their neighbor (thus moving the hole).
  - This is called p-type doping since we have fewer (negatively charged) electrons in the bond holding the atoms together.

---
Making a semiconductor using silicon
Ga
?
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
This atom will accept an electron even
though it is one too many since it fills the
eighth electron position in this shell. Again
this lets current flow since the electron must
come from somewhere to fill this position.

---
Making Silicon into Processors
Start with a very pure ingot of silicon
Carefully add:
  - Phosphorus or Arsenic
  - Gallium or Boron
  - Metal wires

---
Getting Chips out of Wafers

---
Packaging Chips

---
Using doped silicon to make a junction diode
A junction diode allows current to flow in one direction and blocks it in the other.

---
Using doped silicon to make a junction diode
A junction diode allows current to flow in one direction and blocks it in the other.

---
Using doped silicon to make a junction diode
Free Electrons (Ntype) fill Holes (Ptype)‏

---
Using doped silicon to make a junction diode
A depletion zone is made with atoms with completed outer shells (and with a charge)‏

---
Using doped silicon to make a junction diode
With no current, equilibrium occurs with the depletion zone acting as an insulator

---
Using doped silicon to make a junction diode
Connect N-type to native; ptype to positive and the depletion zone shrinks and current flows

---
Making a transistor
Our first level of abstraction is the transistor. (basically 2 diodes sitting back-to-back)‏
P-type
Gate

---
Making a transistor
Transistors are electronic switches connecting the source to the drain if the gate is “on”.
http://www.intel.com/education/transworks/INDEX.HTM
Vcc
Vcc
Vcc

---
Abstractions in CS (gates)‏
Basic Gate: Inverter
Truth Table
I
O
0
1
1
0
I
O
GND
I
O
Vcc
Resister (limits conductivity)‏

---
Abstractions in CS (gates)‏
Truth Table
I
O
0
1
1
0
I
O

---
Abstractions in CS (gates)‏
Basic Gate: Nand (Negated AND)‏
Truth Table
A
B
0
0
1
1
0
1
0
1
1
1
1
0
Y
A
B
Y
GND
A
B
Y
Vcc

---
Abstractions in CS (gates)‏
Basic Gate: And
Truth Table
A
B
Y
A
B
0
0
1
1
0
1
0
1
0
0
0
1
Y

---
Abstractions in CS (gates)‏
Other Basic Gates: Or gate
Truth Table
A
B
Y
A
B
0
0
1
1
0
1
0
1
0
1
1
1
Y

---
Abstractions in CS (gates)‏
Other Basic Gates: Xor gate
Truth Table
A
B
Y
A
B
0
0
1
1
0
1
0
1
0
1
1
0
Y

---
All 2 input 1 output gates (1-8)‏
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
A
B
0
0
1
1
0
1
0
1
0
0
0
1
Y
A
B
0
0
1
1
0
1
0
1
0
0
0
0
Y
A
B
0
0
1
1
0
1
0
1
0
0
1
1
Y
A
B
0
0
1
1
0
1
0
1
0
0
1
0
Y
A
B
0
0
1
1
0
1
0
1
0
1
0
1
Y
A
B
0
0
1
1
0
1
0
1
0
1
0
0
Y
A
B
0
0
1
1
0
1
0
1
0
1
1
1
Y
A
B
0
0
1
1
0
1
0
1
0
1
1
0
Y

---
All 2 input 1 output gates (9-16)‏
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
Truth Table
A
B
0
0
1
1
0
1
0
1
1
0
0
1
Y
A
B
0
0
1
1
0
1
0
1
1
0
0
0
Y
A
B
0
0
1
1
0
1
0
1
1
0
1
1
Y
A
B
0
0
1
1
0
1
0
1
1
0
1
0
Y
A
B
0
0
1
1
0
1
0
1
1
1
0
1
Y
A
B
0
0
1
1
0
1
0
1
1
1
0
0
Y
A
B
0
0
1
1
0
1
0
1
1
1
1
1
Y
A
B
0
0
1
1
0
1
0
1
1
1
1
0
Y

---
Levels of abstraction
- Quantum level, solid state physics
- Conductors, Insulators, Semiconductors.
- Doping silicon to make diodes and transistors.
- Building simple gates, boolean logic, and truth tables
- Combinational logic: adders, muxes, decoders
- Clocks
- Sequential logic: latches, memory
- State machines
- Processor Control: Machine instructions
Computer Architecture: Defining a set of instructions

---
Abstractions in CS (gates)‏
Basic Gate: Inverter
Truth Table
I
O
0
1
1
0
http://www.howstuffworks.com/boolean.htm
Textbook: See Appendix B
I
O
GND
I
O
Vcc
Resister (limits conductivity)‏

---
Abstractions in CS (gates)‏
Basic Gate: Nand (Negated AND)‏
Truth Table
A
B
0
0
1
1
0
1
0
1
1
1
1
0
Y
A
B
Y
GND
A
B
Y
Vcc

---
Abstractions in CS (gates)‏
Basic Gate: And
Truth Table
A
B
Y
A
B
0
0
1
1
0
1
0
1
0
0
0
1
Y

---
Abstractions in CS (gates)‏
Other Basic Gates: Or gate
Truth Table
A
B
Y
A
B
0
0
1
1
0
1
0
1
0
1
1
1
Y

---
Abstractions in CS (gates)‏
Other Basic Gates: Xor gate
Truth Table
A
B
Y
A
B
0
0
1
1
0
1
0
1
0
1
1
0
Y

---
A little math
Grade School
125
5  100
+ 2  101
+ 1  102
binary numbers
10110
0  20
+ 1  21
+ 1  22
+ 0  23
+ 1  24

---
Adding numbers
Decimal Addition
125
+	237
Binary Addition
1011
+	0001
1
1
1
3
2
6
0
1
1
0

---
Building an adder
Half Adder: Carry bit (C)can use an AND gate	Sum bit (S) can use an XOR gate
Half Adder
Add 2 1-bit numbers
A
B
0
0
1
1
0
1
0
1
0
1
1
0
S
0
0
0
1
C
Half Adder
C
S
A
B

---
Combinational Circuits
Implement Boolean expressions
  - Output is determined exclusively by the input
  - No memory: Output is valid only as long as input is
Half Adder
Decoder
MUX
Select one of multiple
Input line to pass to the output
Add 2 1-bit numbers
Select a single line
given an index
A0 A1 Out 0-3
0 0 1000
1 0 0100
0 1 0010
1 1 0001
A B S C
a b 0 a
a b 1 b
A
B
0
0
1
1
0
1
0
1
0
1
1
0
S
0
0
0
1
C

---
Building a Decoder Circuit
Out3 is just an AND gate
Decoder
Decoder
Select a single line
given an index
A0 A1 Out 0-3
0 0 1000
1 0 0100
0 1 0010
1 1 0001
Out1
Out2
A0
A1
Out3
Out0
A0
0
1
0
1
0
0
1
1
0
0
0
1
A1
Out3
A0
0
1
0
1
0
0
1
1
0
0
1
0
A1
Out2
Out2 would be an AND gate if A0 was inverted
A0
0
1
0
1
0
0
1
1
0
1
0
0
A1
Out1
Invert A1
A0
0
1
0
1
0
0
1
1
1
0
0
0
A1
Out0
Invert A1 and A2

---
Building a Mux
Multiplexor: Input S selects either input A or input B
This is called a 2x1 MUX since it has 2 inputs and 1 output.
How would you build a 4x1 MUX?
MUX
Select one of multiple
Input line to pass to the output
A B S C
a b 0 a
a b 1 b
A
S
B
C
MUX
Is A if S is 0
Is 0 if S is 1
Is 0 if S is 0
Is B if S is 1
Is A if S is 0
Is B if S is 1

---
Combinational Circuits
- Adder is the basic gate of the ALU
- Decoder is the basic gate of indexing
- Mux is the basic gate controlling data movement
Decoder
A0
A1
Out0
Out1
Out2
Out3
A
S
B
C
MUX
Half Adder

---
Propagation through Combinational Gates
Gate outputs do not change exactly when inputs do.
  - Transmission time over wires (~speed of light)‏
  - Saturation time to make transistor gate switch
  - Every combinatorial circuit
  has a propagation delay
  (time between input and
  output stabilization)‏
Electron saturation of
p-type silicon at gate

---
Timing in Combinational Circuits
dG2
dG3
dG1
dG3
Delay of gate G2
A
MUX
S
X
G1
B
G2
G3
X
Y
Y
C
time
What is the input/output delay (or simply, delay) of the MUX?
A
S
B
C

---
How about this Circuit?
A
B
G1
G3
G5
F
C
D
G2
G4
E

---
Levels of abstraction
- Quantum level, solid state physics
- Conductors, Insulators, Semiconductors.
- Doping silicon to make diodes and transistors.
- Building simple gates, Boolean logic, and truth tables
- Combinatorial logic: muxes, decoders, adders
- Clocks
- Sequential logic: latches, memory
- State machines
- Processor Control: Machine instructions
- Computer Architecture: Defining a set of instructions

---
What is storage in a computer?
- Disk Storage: long term non-volatile
- Various other optical or magnetic media
  - CD, DVD, magnetic tape
Memory: short term volatile & non-volatile
  - DRAM, SRAM, FlashRam, etc.
- Cache: fast (temporary) memory volatile
- Register: very fast small memory volatile

---
How can silicon remember anything?
What does it mean to remember?
  - Storage cell (We will design this)‏
  - Operations performed
    - Reset value to 0
    - Set value to 1
  - Ability to read current value
    - Was the last command to set or reset
R S Q
0 0 ?
0 1 1
1 0 0
1 1 ?

---
Feedback in a circuit
O
I

---
Let’s design a “flip flop”
Truth Table (NOR)‏
A
B
Y
Start with a NOR gate
A
B
0
0
1
1
0
1
0
1
1
0
0
0
Y

---
2 NOR gates + feedback makes an RS Flipflop
0
1
S
Truth Table (NOR)‏
Q
0
1
Q
R
S R Q Q
0 0
0 1 0 1
0
1 1
A
B
0
0
1
1
0
1
0
1
1
0
0
0
Y

---
RS Flipflop (set)‏
1
0
S
Truth Table (NOR)‏
Q
1
0
Q
R
S R Q Q
0 0
0 1 0 1
0 1 0
1 1
A
B
0
0
1
1
0
1
0
1
1
0
0
0
Y

---
RS Flipflop (retain value 1)‏
0
0
S
Truth Table (NOR)‏
Q
1
0
Q
R
S R Q Q
0 0 Q Q
0 1 0 1
0 1 0
1 1
A
B
0
0
1
1
0
1
0
1
1
0
0
0
Y

---
RS Flipflop (retain value 0)‏
0
1
S
Truth Table (NOR)‏
Q
0
0
Q
R
S R Q Q
0 0 Q Q
0 1 0 1
0 1 0
1 1
A
B
0
0
1
1
0
1
0
1
1
0
0
0
Y

---
RS Flipflop (don’t do this)‏
1
S
Truth Table (NOR)‏
Q
1
Q
R
S R Q Q
0 0 Q Q
0 1 0 1
0 1 0
1 1 ? ?
What does it mean?
A
B
0
0
1
1
0
1
0
1
1
0
0
0
Y

---
Transparent D Flipflop
D
S
Q
Q
R
Gating
signal
G
Set state
is retained
D G Q Q
0 0 Q Q
0 1 0 1
0 Q Q
1 1 1 0
Next state
is set
D
G
Q

---
A Static Memory Cell
d0
R/W
D
Q
G
Enable

---
Tri-state Logic
The output of a gate can be any of three different states: one, zero or not connected
  - Need to disconnect the circuit. How?
Bus Driver
enable
input
output
Implemented as
a single transistor

---
A 4-Bit Register
d0
d2
R/W
D
Q
G
d1
d3
Enable

---
Addressing Memory Arrays
A0
4X16
DECODER
A1
A2
A3
d0
One of the 24 enable lines is turned ON
Enables
Replaces 16x1 MUX
16 X 1 BIT MEMORY

---
A Scheme with Fewer Components
A0
2x4
DECODER
A1
A2
2x4
DECODER
A3
d0
16 X 1 BIT MEMORY

---
Putting it in a package

---
Other Memories
Static RAM
  - Built from sequential circuits
    - Takes 4-6 transistors to store 1 bit
    - Fast access (< 1 ns access possible)‏
Dynamic RAM
  - Built using a single transistor and a capacitor
    - 1’s must be refreshed often to retain value
    - Slower access than static RAM
    - Much more dense layout than static RAM
ROM, PROM, Flash memory, etc. Later