Lecture 7
Lecture 2
Verilog
  - Structural constructs
  - Describing combinational circuits
- Additional references
  - Tutorial and reference manual are found in ActiveHDL help
  - “Starter’s Guide to Verilog 2001” by Michael Ciletti copies for borrowing in hardware lab

---
Combinational design
Combinational design
Step 1: Understand the problem
  - Identify the inputs and outputs
  - Draw a truth table
Step 2: Simplify the logic (we will get to this)
  - Draw a K-map
  - Write a simplified Boolean expression
    - SOP or POS
    - Use don’t cares
Step 3: Implement the design
  - Logic gates and/or
  - Verilog

---
Ways of specifying circuits
Ways of specifying circuits
Schematics
  - Structural description
  - Describe circuit as interconnected elements
    - Build complex circuits using hierarchy
      - Large circuits are unreadable
Hardware description languages (HDLs)
  - Not programming languages
    - Parallel languages tailored to digital design
  - Synthesize code to produce a circuit

---
Verilog versus VHDL
Verilog versus VHDL
- Both “IEEE standard” languages
- Most tools support both
- Verilog is “simpler”
  - Less syntax, fewer constructs
VHDL is more structured
  - Can be better for large, complex systems
  - Better modularization

---
Simulation and synthesis
Simulation and synthesis
Simulation
  - Models what a circuit does
    - Multiply is “*”, ignoring implementation options
  - Allows you to test design options
  - “Execute” a design to verify correctness
Synthesis
  - Converts your code to a "netlist"
    - Can simulate synthesized design
  - Tools map your netlist to hardware

---
Simulation and synthesis
- Simulation and synthesis:
  - We are using a simulator!
  - The tool can be used to do synthesis.
Synthesis
HDL
Description
Gate or
Transistor
Description
Simulation
Simulation
Physical
Implementation
Functional
Validation
Functional/
Timing
Validation
Real
Chip!

---
Simulation
Simulation
You provide an environment
  - Using non-circuit constructs
    - Active-HDL waveforms, read files, print
  - Using Verilog simulation code
    - A “test fixture”
Simulation
Test Fixture
(Specification)
Circuit Description
(Synthesizable)

---
Specifying circuits in Verilog
Specifying circuits in Verilog
Three major styles
  - Instances and wires
  - Continuous assignments
  - “always” blocks
“Behavioral”
“Structural”
wire E;
and #2 g1(E,A,B);
not #1 g2(Y,C);
or #2 g3(X,E,Y);
wire E;
assign #2 E = A & B;
assign #1 Y = ~C;
assign #2 X = E | Y;
reg E, X, Y;
always @ (A or B or C)
begin
E = A & B;
Y = ~C;
X = E | Y;
end

---
Data types
Data types
Values on a wire
  - 0, 1, x (unknown or conflict), z (tristate or unconnected)
Vectors
  - A[3:0]	vector of 4 bits: A[3], A[2], A[1], A[0]
    - Unsigned integer value
    - Indices must be constants

---
Delays
Identified by the #<num>
  - and #2 g1(E,A,B);
  - Means it take 2 gate delays to assign E = A & B.
Used to determine the how long a circuit takes to saturate.

---
Manipulating vectors
Manipulating vectors
Concatenating bits/vectors, use { }
  - e.g. sign extend
    - B[7:0] = {A[3], A[3], A[3], A[3], A[3:0]};
    - B[7:0] = {4{A[3]}, A[3:0]};
- Style: Use	a[7:0] = b[7:0] + c[7:0]	Not a = b + c;

---
Data types that do NOT exist
Data types that do NOT exist
- Structures
- Pointers
- Objects
- Recursive types
Verilog is not C or Java or Lisp or …!

---
Numbers
Numbers
- Format: <sign><size><base><number>
- 14
  - Decimal number
–4’b11
  - 4-bit 2’s complement binary of 0011 (is 1101)
12’b0000_0100_0110
  - 12 bit binary number (_ is ignored)
12’h046
  - 3-digit (12-bit) hexadecimal number

---
Numbers are unsigned
Numbers are unsigned
C[4:0] = A[3:0] + B[3:0];
  - if A = 0110 (6) and B = 1010(–6), then C = 10000 (not 00000)
  - B is zero-padded, not sign-extended

---
Operators
Operators
Similar to C operators

---
Two abstraction mechanisms
Two abstraction mechanisms
Modules
  - More structural, but also behavioral
  - Heavily used “real” Verilog code
Functions
  - More behavioral
  - Used to some extent in “real” Verilog

---
Basic building blocks: modules
Basic building blocks: modules
// first simple example
module simple (A, B, C, X, Y);
input A, B, C;
output X, Y;
wire E;
and #2 g1(E, A, B);
not #1 g2(Y, C);
or #2 g3(X, E, Y);
endmodule

---
Basic building blocks: modules
Instanced into a design
  - Never called
- Use wires for connections
- Modules execute in parallel
- Gate declarations (and, or, etc)
  - List outputs first
  - Inputs second
- Name can’t begin with a number
- Names are case sensitive
- Keywords are in lowercase
- and, or, not are keywords
- Illegal to nest module definitions
- // for comments

---
Modules are circuit components
Modules are circuit components
Module has ports
  - External connections
  - A,B,C,X,Y in example
Port types
  - input
  - output
  - inout (tristate)
Use assign statements for Boolean expressions
  - and  &
  - or  |
  - not  ~
// previous example as a
// Boolean expression
module simple2 (A,B,C,X,Y);
input A,B,C;
output X,Y;
assign #4 X = (A&B)|~C;
assign #1 Y = ~C;
endmodule

---
Testing your circuits
module simple_test();
reg in1, in2, in3;
wire X, Y;
simple DUT(in1, in2, in3, X, Y);
initial
begin
in1 <= 0;
in2 <= 0;
in3 <= 0;
#7
$display("X = %d, Y = %d", X, Y);
end
endmodule
- Very important!
- Create a test module!
  - Separate file
  - Compile both modules together
  - Use print statements to debug.
  - Common to use ‘DUT’ (Device Under Test)
  - To name the module.
- Use behavioral model to test
  - For simplicity.

---
Structural Verilog
Structural Verilog
module xor_gate (a,b,out);
 input a,b;
 output out;
 wire abar, bbar, t1, t2;
 not #1 inva (abar,a);
 not #1 invb (bbar,b);
 and #2 and1 (t1,abar,b);
 and #2 and2 (t2,bbar,a);
 or #2 or1 (out,t1,t2);
endmodule
8 basic gates (keywords):
and, or, nand, nor
buf, not, xor, xnor

---
Behavioral Verilog
Behavioral Verilog
Describe circuit behavior
  - Not implementation
module full_addr (Sum,Cout,A,B,Cin);
 input A, B, Cin;
 output Sum, Cout;
 assign {Cout, Sum} = A + B + Cin;
endmodule
{Cout, Sum} is a concatenation
A
B
Cin
Cout
Sum
Adder

---
Behavioral 4-bit adder
Behavioral 4-bit adder
module add4 (SUM, OVER, A, B);
input [3:0] A;
input [3:0] B;
output [3:0] SUM;
output OVER;
assign {OVER, SUM[3:0]} = A[3:0] + B[3:0];
endmodule
Buses are implicitly connected—
If you write BUS[3:2], BUS[1:0],
they become part of BUS[3:0]
“[3:0] A” is a 4-wire bus labeled “A”
Bit 3 is the MSB
Bit 0 is the LSB
Can also write “[0:3] A”
Bit 0 is the MSB
Bit 3 is the LSB

---
Continuous assignment
Continuous assignment
Assignment is continuously evaluated
  - Corresponds to a logic gate
  - Assignments execute in parallel
assign A = X | (Y & ~Z);
assign B[3:0] = 4'b01XX;
assign C[15:0] = 16'h00ff;
assign #3 {Cout, Sum[3:0]} = A[3:0] + B[3:0] + Cin;
gate delay (used by simulator)
Boolean operators
(~ for bit-wise negation)
bits can assume four values
(0, 1, X, Z)
variables can be n-bits wide
(MSB:LSB)

---
Invalid sequential assigns
Invalid sequential assigns
assign A = X | (Y & ~Z);
assign B = W | A;
assign A = Y & Z;
“Reusing” a variable on the left
side of several assign statements
is not allowed
assign A = X | (Y & ~Z);
assign B = W | A;
assign X = B & Z;
Cyclic dependencies also are bad
A depends on X
which depends on B
which depends on A

---
Example: 4-bit comparator
Example: 4-bit comparator
module Compare1 (A, B, Equal, Alarger, Blarger);
1. input A, B;
2. output Equal, Alarger, Blarger;
3. wire notB, notA, AandB, NotAandB;
4. not #1 n1(notA, A);
5. not #1 n1(notB, B);
6. and #2 g1(AandB, A, B);
7. and #2 g2(NotAandB, notA, notB);
8. or #2 g3(Equal, AandB, NotAandB);
9. and #2 g4(Alarger, A, notB);
10. and #2 g5(Blarger, notA, B);
11. endmodule
Starting with 1-bit comparator
  - Top-down design and bottom-up design are both okay
  - Module ordering doesn’t matter because modules execute in parallel

---
4-bit comparator
4-bit comparator
1. // Make a 4-bit comparator from 4 1-bit comparators
   module Compare4(A4, B4, Equal, Alarger, Blarger);
    input [3:0] A4, B4;
    output Equal, Alarger, Blarger;
    wire e0, e1, e2, e3, Al0, Al1, Al2, Al3, B10, Bl1, Bl2, Bl3;
2. wire Al2ande3, Al1ande3ande2, Al0ande3ande2ande1;
3. wire NotAlarger, NotEqual;
    Compare1 cp0(A4[0], B4[0], e0, Al0, Bl0);
    Compare1 cp1(A4[1], B4[1], e1, Al1, Bl1);
    Compare1 cp2(A4[2], B4[2], e2, Al2, Bl2);
    Compare1 cp3(A4[3], B4[3], e3, Al3, Bl3);
    and #4 (Equal, e0, e1, e2, e3);
4. not #1 (NotEqual, Equal);
5. and #2 (Al2ande3, Al2, e3);
6. and #4 (Al1ande3ande2, Al1, e3, e2);
7. and #4 (Al0ande3ande2ande1, Al0, e3, e2, e1);
8. or #4 (Alarger, Al3, Al2ande3, Al1ande3ande2, Al0ande3ande2ande1);
9. not #1 (NotAlarger, Alarger);
10. and #2 (Blarger, NotAlarger, NotEqual);
    endmodule

---
Functions
Functions
Use functions for complex combinational logic
module and_gate (out, in1, in2);
 input in1, in2;
 output out;
assign out = myfunction(in1, in2);
function myfunction;
input in1, in2;
begin
myfunction = in1 & in2;
end
endfunction
endmodule
Benefit:
Functions force a result
 Compiler will fail if function
does not generate a result

---
Always code blocks
Always code blocks
reg A, B, C;
always @ (W or X or Y or Z)
begin
A = X | (Y & ~Z);
B = W | A;
A = Y & Z;
if (A & B) begin
B = Z;
C = W | Y;
end
end
Statements in an always block are executed in sequence
Sensitivity list:
block is executed
each time one of
them changes value
Variables that appear on the left hand side in an always block must be declared as “reg”s
BAD: All variables must be assigned on every control path!!!

---
Assignments
Assignments
Blocking assignments (Q = A)
  - Variable is assigned immediately
    - New value is used by subsequent statements
Non-blocking assignments (Q <= A)
  - Variable is assigned after all scheduled statements are executed
    - Value to be assigned is computed but saved for later parallel assignment
  - Usual use: Register assignment
    - Registers simultaneously take new values after the clock edge

---
Blocking vs. non-blocking
Blocking vs. non-blocking
Example: Swap
always @(posedge CLK)
begin
temp = B;
B = A;
A = temp;
end
always @(posedge CLK)
begin
A <= B;
B <= A;
end

---
Verilog tips
Verilog tips
Do not write C-code
  - Think hardware, not algorithms
    - Verilog is inherently parallel
    - Compilers don’t map algorithms to circuits well
Do describe hardware circuits
  - **First draw a dataflow diagram!!!
  - Then start coding

---
Verilog tips
- always statement : Sequential Block
- Sequential Block: All statements within the block are executed sequentially
- When is it executed?
  - Occurrence of an event in the sensitivity list
  - Event: Change in the logical value
- Statements with a Sequential Block: Procedural Assignments
- Delay in Procedural Assignments
  - Inter-Statement Delay
  - Intra-Statement Delay

---
Verilog tips
- Inter-Assignment Delay
  - Example:
    - Sum = A ^ B;
- #2 Carry = A & B;
  - Delayed execution
- Intra-Assignment Delay
  - Example:
- Sum = A ^ B;
- Carry = #2 A & B;
  - Delayed assignment

---
Verilog tips
- Two Procedural Constructs
- initial Statement
- always Statement
- initial Statement : Executes only once
- always Statement : Executes in a loop
- Example:
…
always @(A or B) begin
Sum = A ^ B;
Carry = A & B;
end
…
…
initial begin
Sum = 0;
Carry = 0;
end
…

---
Verilog tips
- always statement : Sequential Block
- Sequential Block: All statements within the block are executed sequentially
- When is it executed?
  - Occurrence of an event in the sensitivity list
  - Event: Change in the logical value
- Statements with a Sequential Block: Procedural Assignments
- Delay in Procedural Assignments
  - Inter-Statement Delay
  - Intra-Statement Delay